## Slide 1: Smart Water Management for Urban Green Infrastructure
SMART CITIES · WATER DOMAIN
A low-cost, network-resilient edge-IoT irrigation node with deep-learning soil analysis
Project Report & Demonstration · Design of Smart Cities
Notes: Title slide. Introduce the project as sitting in the water domain of smart city design, not as an agriculture project.

## Slide 2: Cities irrigate a great deal of land — on a timer
Parks, urban forests, road medians, green belts, green roofs and community gardens
A timer cannot sense
It does not know it rained yesterday, or that one bed drains faster than another.
Both failures at once
The same green space is over-watered in places and under-watered in others.
Nobody notices
Open-loop systems report success whether or not water actually reached the soil.
Green infrastructure is growing in importance — vegetation moderates the urban heat island, manages stormwater and improves air quality. Cities are asked to maintain more of it, more reliably, without using more water.
Demand-driven irrigation is the direct response to that pressure.
Notes: Frame the problem in the civic water domain. The key point is that open-loop timer irrigation produces over- and under-watering simultaneously, and reports success either way.

## Slide 3: What we built
One node per irrigation zone, replicated across heterogeneous urban green space
₹970
cost per node
1 Hz
local decision rate
0
network dependency
Notes: The node is deliberately generic across site types. Emphasise: each site closes its own loop; telemetry flows up, commands never flow down.

## Slide 4: SRS — Requirements
SECTION ONE
Software Requirements Specification — what the system must do, and what it must survive

## Slide 5: SRS — Requirements
Ten functional and six non-functional requirements; the non-functional ones decide whether it scales
Functional
Measure soil moisture, air temperature and humidity
Switch the pump automatically from the measurement
Use two thresholds with a dead band, not one set point
Emit a telemetry record at a fixed interval
Indicate state locally, visible without instruments
Classify soil type and condition from a photograph
Produce weather-aware watering advice
Provide monitoring, reporting and manual override
Non-functional
The irrigation decision is taken on the node, never remotely
Unit cost low enough to deploy in quantity
Failure of a secondary sensor must not stop irrigation
The monitoring layer must be incapable of actuation
Commodity parts, for municipal procurement and repair
Undetectable failure modes must be identified and documented
Notes: Stress NFR-1 and NFR-4: these are the requirements that distinguish a city deployment from a single demo unit.

## Slide 6: SDS — Design
SECTION TWO
Software Design Specification — architecture, hardware, data and the control law

## Slide 7: Four layers, one boundary that matters
Everything needed to keep vegetation watered lives on the microcontroller. Every layer above it is additive: logging, classification, advice, reporting.
Notes: Walk the four layers quickly. The point to land is the boundary: the host can observe everything and command nothing.

## Slide 8: The node never asks a server whether to irrigate
CENTRAL DESIGN DECISION
On a farm that is convenience. Across a fleet of four hundred nodes it is the difference between a network outage degrading visibility and a network outage stopping service.
Network fails
Every node keeps watering
Host fails
Every node keeps watering
Node fails
One zone affected, not the fleet
Notes: This is the slide to slow down on. It is the smart-city argument: adding visibility must not add a single point of failure.

## Slide 9: Hardware and cost
Commodity parts only — unit cost is a design parameter, not an outcome
Bill of materials
ESP32-WROOM-32 | ₹284
Capacitive probe v1.2 | ₹83
DHT11 module | ₹61
5 V relay module | ₹42
Pump, BC547B, LEDs, resistors, wiring | ₹500
Total per node | ₹970
100 zones ≈ ₹97,000 400 zones ≈ ₹3.9 lakh
Hardware only — excludes enclosures, plumbing, installation and maintenance. Given to show the order of magnitude at which this becomes a procurement question.
Notes: Be explicit that the scale figures are arithmetic on unit cost and exclude installation. Do not overclaim.

## Slide 10: Implementation
SECTION THREE
Firmware, host software and the assembled node

## Slide 11: The control loop, once per second
Self-contained: no host, no network, no cloud service
1
Read sensors
DHT11 on GPIO 4, capacitive probe on GPIO 34 as a raw 12-bit value
2
Convert and clamp
Two-point calibration to 0–100 %; the clamp also guards a disconnected probe
3
Apply hysteresis
Pump on below 30 %, off above 60 %, hold state in between
4
Update indicators
Red steady for alive; green blinks at 250 ms while the pump runs
5
Emit telemetry
One JSON record at 115200 baud, then wait one second
Stack
C/C++ on the Arduino core
USB serial, 115200 baud, JSON
Python 3.11 + pyserial
TensorFlow / Keras
scikit-learn
Streamlit + Plotly
ReportLab
Open-Meteo forecast API
Notes: If the DHT11 read fails, nulls are sent and irrigation continues on moisture alone. That is NFR-3 in the firmware.

## Slide 12: The assembled node
Probe in a sealed soil container that can be wetted and left to dry — repeatable control of the variable under test
Notes: Point out the separate 5 V supply for the pump and the common ground. Good slide to hand over to the demo video.

## Slide 13: Testing
SECTION FOUR
Not only whether it works, but what it cannot see

## Slide 14: Seven fault-injection tests
Five behaved as specified; two did not, and both are reported
Test | Condition applied | Result
TC-01 | Moisture 65 %, normal conditions | Pump off, telemetry sent — pass
TC-02 | Moisture 22 % | Pump on, green LED blinking — pass
TC-03 | Moisture 45 % with pump already on | State held, no chatter — pass
TC-04 | Moisture exactly 30 % | Pump off, matches the rule — pass
TC-05 | DHT11 data line removed | Nulls sent, irrigation continued — pass
TC-06 | Moisture probe unplugged | Fail-safe triggered, but fault not detected
TC-07 | Pump supply removed while running | Pump stopped, firmware kept reporting it on
TC-07 is the most consequential result. The relay is commanded but never measured, so a dead pump is reported as running. In a municipal deployment this persists until vegetation visibly declines — and every record in between says the site was watered.
Notes: Do not skip past TC-06 and TC-07. Examiners respect a team that found its own failure modes.

## Slide 15: Control-law validation
8,171 telemetry records across 33 logging sessions, median interval 1.00 s
17 %
fewer relay transitions
than a single set point
6.6 %
of readings fall inside
the 30–60 % dead band
Notes: The benefit is moderate because the probe spends little time in the dead band. Across a continuously running municipal fleet, 17 percent fewer actuations accumulates into relay and pump service life.

## Slide 16: How the soil classifier was evaluated
The same classifier and features, tested two ways
Two protocols
Augmentation-level Shuffle all expanded samples, then split. Near-identical crops of one photograph land on both sides. Source-disjoint Hold out whole photographs. The classifier is tested only on soil it has never seen.
Soil type falls from 91.9–94.0 % to 44.6–46.8 % — close to the 43.3 % obtainable by always guessing the most common class. Most of the apparent accuracy came from recognising photographs, not soils. Soil condition holds up at 75.5–86.1 % and is the usable one.
Notes: Held across three network architectures and five randomisations, so it is a property of the dataset, not one model. Only 16 source photographs, two classes with a single photograph each.

## Slide 17: Outcome
SECTION FIVE
What was achieved, what was not, and what it means at city scale

## Slide 18: Measured outcomes
15 of 16 requirements fully met; one partially met
₹970
per node
17 %
fewer actuations
5 / 7
fault tests passed
8,171
records logged
86.1 %
soil condition, unseen
46.8 %
soil type, unseen
The infrastructure objective was met. The analytics objective is qualified: soil condition is usable, soil type is not — and would have looked highly accurate under conventional evaluation.

## Slide 19: What this means at city scale
Visibility without fragility
Because the monitoring layer has no actuation path, adding city-wide visibility does not add a city-wide failure mode. An operations centre can lose four hundred nodes from view without any of them stopping work.
Cost decides coverage
At ₹970 a node, the limiting factor on how much green space a city can instrument stops being hardware budget and becomes installation and maintenance.
Silent failure is a governance problem
A dashboard showing green for a dead pump is worse than no dashboard. Undetectable failure modes must be found before deployment, not after.
Accuracy claims need protocols
Smart-city systems increasingly justify decisions by citing model accuracy. A figure quoted without stating how the data were split cannot support a procurement decision.

## Slide 20: Limitations and next steps
Limitations
A pump that loses power is reported as running
A drifted or fouled probe is trusted
Water saving not measured — no flow meter fitted
Soil type not deployable at its measured accuracy
Validated in a container, not a live municipal site
One probe represents a whole irrigation zone
Telemetry link is wired USB serial
Next steps
ACS712 current sensor — ₹145, closes the TC-07 gap
Pulse-response probe check to catch a fouled probe
Inline flow meter, so saving is reported in litres
Wi-Fi, LoRaWAN or NB-IoT backhaul for real city scale
Multi-zone valve control from one node
Several hundred field photographs for the classifier
Integration with municipal asset-management workflow
Notes: The ACS712 is the highest-value single addition: about 15 percent of unit cost, and it removes the one failure the system cannot see.

## Slide 21
IN CLOSING
A controller that reports irrigation it is not performing,
and a classifier that reports accuracy it does not have,
fail in the same way
Both look correct from the outside. Neither was discovered by watching the system work — both were found only by testing specifically for them. For infrastructure a city intends to trust without supervision, that testing is not an optional extra.
Thank you